Type BBVS-60 Manufacturer Beijing GangZhen Mechanical 6 Electronic Technology Co. Ltd Address No. 20 Jinxing Rd, Daxing district, Beijing 102628, China Phone (Fax) ++86-10-60212319 (-37) E-mail geodevice@sina.com Homepage http://www.geodevice.cn/ Category Force-balance broadband, three component Flat response Velocity 16.7 mHz (60 s) to 50 Hz Resolution: NLNM 16.7 mHz to 8 Hz within 10 dB of NLNM 8 mHz to 20 Hz within 20 dB of NLNM 5 mHz to 50 Hz Operating range ±10 mm/s Generator constant 2000 Vs/m Output differential, ±10 V per line Weight 12 kg Size 24 cm dia., 27 cm high Power 9 to 18 volts, 1.1 watts Manual control Mass lock Remote control centering Remote diagnostic Mass position Accessories Tools, thermal insulation Typical installation All purpose Data Sheet http://www.geodevice.cn/en/productInfo.aspx?n= 20090921143217421562 Remarks This instrument uses an astatic leaf-spring suspension like the Streckeisen seismometers.