Type CMG-3T, CMG3-TB (borehole) Manufacturer Guralp Systems Limited Address 3 Midas House, Calleva Park, Aldermaston, Reading RG7 8EA, UK Phone ++44 118 9819056 E-mail sales@guralp.com Homepage www.guralp.com Category Force-balance VBB, three-component Flat response velocity 8.33 mHz (120 s) to 50 Hz (others available) Resolution: NLNM 30 mHz to 18 Hz* within 10 dB of NLNM 5 mHz to 30 Hz* within 20 dB of NLNM 3 mHz to 50 Hz* Operating range 13 mm/s Generator constant 1500 Vs/m (others available) Output differential, 10 V per line Weight 14 kg Size 17 cm dia., 34 cm high Power 10 to 30 volts, 0.75 watts Manual control - Remote control mass lock, centering, calibration Remote diagnostic mass position Accessories control and breakout box Typical installation observatory, vault, and field use Data sheet http://www.guralp.com/products/3T/ Remarks Tight thermal shielding recommended. Until recently the CMG-3T was one of the two most widely used broadband seismometers (the other one being the STS-2). The noise data are from the borehole version CMG-3TB. * based on Ringler and Hutt 2010. Resolution above 10 Hz is extrapolated; data from the borehole version.