Type FSS-3M, FSS-3DBH Manufacturer Beijing GangZhen Mechanical 6 Electronic Technology Co. Ltd Address No. 20 Jinxing Rd, Daxing district, Beijing 102628, China Phone (Fax) ++86-10-60212319 (-37) E-mail geodevice@sina.com Homepage http://www.geodevice.cn/ Category Force-balance short-period, three component Surface (M) and borehole (DBH) packages Flat response Velocity 0.5Hz to 70 Hz Resolution: NLNM 0.2 Hz to 6 Hz within 10 dB of NLNM 0.2 Hz to 10 Hz within 20 dB of NLNM Operating range ±10 mm/s Generator constant 2000 Vs/m Output differential, ±10 V per line Weight 12 kg (FSS-3M), 8 kg (FSS-3BH) Size 240 mm dia., 270 mm high (FSS-3M) 10 cm dia., 80 cm high (FSS-3BH) Power 9 to 18 volts, 0.6 watts Manual control No centering necessary. No mass lock? Remote control Remote diagnostic Accessories Typical installation All purpose. FSS-3BH is a borehole version. Data Sheet http://www.geodevice.net/FSS-3DBH.asp Remarks Widely used in China. According to the data sheet, the displacement transducer is electromagnetic (must be an LVDT) – quite unusual for a short-period seismometer.