Type OYO-Geospace GS-1 Manufacturer OYO Geospace Address 7007 Pinemont, Houston, Texas 77040,USA Phone ++1-713-986-4444 Fax: -8723 E-mail sales@oyogeospace.com Homepage http://www.oyogeospace.com/technologies Category Passive electromagnetic single-component short-period Flat response Velocity 1 Hz to >100 Hz (2 Hz version is available) Resolution: NLNM 0.11 to 15 Hz with low-noise preamplifier* within 10 dB of NLNM 0.07 to 50 Hz with low-noise preamplifier* within 20 dB of NLNM 0.05 to 150 Hz with low-noise preamplifier* Operating range large, limited by preamplifier Generator constant 275 Vs/m with 4550 Ohms coil output differential, unlimited Weight 2 kg. Moving mass is 0.7 kg. Size 8 cm dia. , 16 cm high Power - Manual control no mass lock required. Short signal coil and tilt the instrument for transportation. Remote control - Remote diagnostic - Accessories - Typical installation temporary installations, field work Data sheet http://www.geospacelp.com/index.php?id=169 Remarks A three-component package is available as “Seis-Monitor” * based on circuit analysis with op-amp LT1007 as a preamplifier. Low-noise model may be inaccurate above 10 Hz.