Type KS-1 Manufacturer Geotech Instruments LLC Address 10755 Sanden Drive, Dallas, Texas 75238-1336, USA Phone (001) 214 221 0000 E-mail info@geoinstr.com Homepage www.geoinstr.com/ Category Force-balance VBB, three-component Flat response velocity 3 mHz (330 s) to 5 Hz Resolution: NLNM 10 mHz to 5 Hz* within 10 dB of NLNM 4 mHz to 9 Hz* within 20 dB of NLNM 0.3 mHz to 12 Hz* Operating range 8 mm/s Generator constant 2400 Vs/m Output differential, 10 V per line Weight 43 kg Size 27 cm dia., 34 cm high Power 24 V, 2.4 W Manual control - Remote control mass lock, centering, calibration Remote diagnostic mass position Accessories - Typical use Observatory Data sheet http://www.geoinstr.com/ds-ks1.pdf Remarks This is the same system as the KS54000 borehole seismometer but packaged in two separate units (mechanical sensors and electronics) for surface installation. * based on Ringler and Hutt 2010.