Type Le-3d lite Manufacturer Lennartz Electronic Address Bismarckstrasse 136, D-72072 Tuebingen, Germany Phone ++49 7071 93550 E-mail info@lennartz-electronic.de Homepage www.lennartz-electronic.de Category Active short-period, three-component Flat response velocity 1 to 80 Hz Resolution: NLNM --- within 10 dB of NLNM 0.2 to 0.5 Hz (microseismic peak) within 20 dB of NLNM 0.15 to 20 Hz Operating range 13 mm/s below 4.5 Hz, decreasing at higher freq. Generator constant 400 Vs/m Output 5 V single-ended Weight 1.8 kg Size 95 mm dia., 65 mm high Power 12 V, 0.1 W Manual control no mass lock required Remote control calibration Remote diagnostic - Accessories - Typical installation monitoring networks, field deployment Data sheet http://www.lennartz-electronic.de/MamboV4.5.2/index.php? option=com_content&task=view&id=72&Itemid=55 Remarks A very small and rugged three-component, short-period, active seismometer. The sensor is a commercial 4.5 Hz geophone whose response is electronically extended by a negative damping resistance (a form of negative feedback). Not as sensitive as larger seismometers but good enough where ground noise is not extremely low. A single-component version Le-1d is also available. Higher performance is offered by the Le-3d/5s and Le-3d/20s.