Type PMD BB 603 Manufacturer Precision Measurement Devices Address 105F W. Dudleytown Rd., Bloomfield, CT 06002, USA Phone ++1 860 242 8177 E-mail sales@pmdsci.com Homepage http://www.pmdsci.com/ Category Molecular-electronic BB three-component, with force feedback Flat response velocity 16.7 mHz (60 s) to 50 Hz Resolution: NLNM 0.05 Hz (20 s) to 5 Hz (manufacturer) within 10 dB of NLNM within 20 dB of NLNM Operating range 10 mm/s at low frequencies Generator constant 2000 Vs/m (other values optional) Output differential, 10 V per line Weight 11 kg Size 20 cm dia., 22 cm high Power 9 – 30 volt, 35 mW; low-power version (15 mW) available Manual control No mass lock or centering required Remote control Calibration, gain setting over serial port (optional) Remote diagnostic - Accessories - Typical installation battery-powered stations, harsh environments. borehole and OBS versions available. Data sheet http://www.pmdsci.com/pdfs/BB603.pdf Remarks An unconventional sensor. The horizontals are essentially circular-tube tiltmeters where the flow of an electrolyte through a platinum mesh is measured using the MET effect (molecular-electronic transfer, also used in the “solion” transducer). The vertical sensor supports a column of electrolyte in a vertical tube with a membrane and a spring. These sensors have extremely low power consumption, are very rugged, need not be locked or leveled; they simply start working after power-on. Their performance in other respects is however inferior to force-balance sensors.