Type Trillium Compact Manufacturer Nanometrics Inc. Address 250 Herzberg Road, Kanata, Ontario, Canada K2K 2A1 Phone ++1 613 592 6776 E-mail info@nanometrics.ca Homepage http://www.nanometrics.ca/ Category Miniature Force-balance BB, symmetric-triaxial Flat response velocity 8.3 mHz (120 s) to 100 Hz Resolution: NLNM 50 mHz to 8 Hz* within 10 dB of NLNM 45 mHz to 20 Hz* within 20 dB of NLNM 30 mHz to 50 Hz* Operating range ±26 mm/s Generator constant 750 Vs/m Output differential, ±10 V per line Weight comparable to a 1 Hz geophone Size comparable to a 1 Hz geophone Power 9 to 36 volt, 0.16 watt Manual control none: no mass lock or centering required Remote control RS-232 compatible integrated web server, UVW selection Remote diagnostic mass positions, temperature, serial number, poles and zeros Accessories - Typical installation temporary installations, field work Data sheet http://www.nanometrics.ca/products/trillium-compact Remarks OBS and all-terrain versions with internal self-leveling gimbal are available. * based on Ringler and Hutt 2010 and the manufacturer