Type Trillium 120 P / PA Manufacturer Nanometrics Inc. Address 250 Herzberg Road, Kanata, Ontario, Canada K2K 2A1 Phone ++1 613 592 6776 E-mail info@nanometrics.ca Homepage http://www.nanometrics.ca/ Category Force-balance VBB, symmetric-triaxial Flat response velocity 83 mHz (120 s) to 145 Hz Resolution: NLNM 25 mHz to 12 Hz* within 10 dB of NLNM 4 mHz to 20 Hz* within 20 dB of NLNM <0.3 mHz to 50 Hz* Operating range ± 16 mm/s Generator constant 1200 Vs/m Output differential, ±10 V per line Weight 7.5 kg Size 21 cm dia., 22 cm high Power 9 to 36 volt, 0.62 watt Manual control centering (120P). No mass lock required. Motorized mass centering (120PA). Remote control centering, UVW/XYZ mode, short/long period mode, firmware updates Remote diagnostic mass positions, temperature, serial number, status Accessories - Typical installation all purpose Data sheet http://www.nanometrics.ca/products/trillium-120-ppa Remarks Large temperature range without re-centering (±45o). A posthole version with remote leveling is available. * based on Ringler and Hutt 2010 and the manufacturer